Genesis 65XX macro and cross assembler Version 2.2
		   &  Genesis 65XX resourcer alpha version
		(c) 1994-96 by Sven Michael Klose, Bielefeld.

This is free software and a part of the TMA project. Please read COPYING
for details.

FTP:	copei.devcon.net/pub/tma
Emai:	sven@devcon.net


ÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
³ Contents			     ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

 Introduction :
 What is Genesis ? ................................................... 1-0
 Assembing the first source .......................................... 1-1
 Executing the assembled program ..................................... 1-2
 Transfer to other platforms ......................................... 1-3

 Programming Genesis :
 Syntax of the assembler ............................................. 2-0
 Syntax of the 65XX mnemonics ........................................ 2-1
 Labels .............................................................. 2-2
 Mnemonics ........................................................... 2-3
 Operands ............................................................ 2-4
 Byte/word syntax .................................................... 2-4-1
 Arithmetic operations ............................................... 2-4-2
 Comments ............................................................ 2-5
 Directives .......................................................... 2-6
 Error messages ...................................................... 3-0

 The 65XX CPU:
 The 65XX instruction set in alphabetical order ................. Appendix A
 Mnemonics of the undocumented instructions ..................... Appendix B
 Opcodes of the undocumented instructions ....................... Appendix C
 History of Genesis ............................................. Appendix D

What is Genesis ?
==================

Genesis is a cross assembler for 65x0 CPUs with an amazing turn of speed.
It is able to produce binary and tape files for the "real C64 emulator".
Now it's able to assemble undocumented commands even in the shareware
version.
For modular programming Genesis knows include files.
Macros are available only in the registered version.


1.1 Introduction
========================

Start a trial run with the delivered source file :

GENESIS GAME.A65 GAME.BIN


1.2 How the ‡¤¦¨ can I use the code then ?
==========================================================

No problem ! But you should own the *real* C64-Emulator written by
Miha Peternel and it should be installed on your hard disk ...
The PC64 emulator doesn't handle T64 files but you can use raw files.

Type in

GENESIS GAME.A65 c:\C64_EMU\GAME.T64
or 
GENESIS GAME.A65 C:\C64_EMU\GAME.BIN for PC64.

Perhaps you'll have to modify the directory name.
Genesis now assembles the code and writes it to disk
as a tape file for the emulator.

Now start the emulator und type LOAD without the RETURN-Key 
then press the F9-key and choose

GENESIS 2.2 CREATED TAPE 
 and
GENESIS 2.2 FILE

Finally type the RUN command. Bad luck ...


1.3 Other ways of using Genesis 6510 
=====================================

To transfer your assembled programs easily use one of your
serial or parallel ports of your personal computer.
The handling of Genesis is easy in this way, too.
Type in

GENESIS GAME.A65 COM1

to let Genesis put out the assembled code to COM1.
Anyway, you'll have to link your PC with your good, ol' C64
and you'll have to write a C64 program which receives the data
and writes it to memory or to disk. FIXME.

----------------------------------------------------------------------------


2.2 Syntax of 6510 mnemonics
============================

Genesis accepts more or less standard syntax.
The structure is always the same:

Label:	Mnemonic:  Operand:    Comment:
------------------------------------------------------------------
label	lda	   #$00        ; load accumulator with 0




2.2 Labels
==========

A label always begins with a letter and ends with a space char.
Never use chars which are reserved for operands.
For example :

WriteChar-1
Hello$
A&bs	 will force error messages.

If you can define many labels with ONE adress. For example:

	     pointer xpos overbyte BYT 0

if you want to save memory.


2.3 Mnemonics
=============

This version accepts standard mnemonics and undocumented mnemonics,
adressing modes, all mnemonics of the 65xx series and it contains a
documentation file with an exact list of their opcodes and timing.


2.4 Operands
============

Following adressing modes are legal :

Adressing mode: 	Example:
---------------------------------
Implied.		ASL
Immediate		LDA #$ff
Zero paged		LDA $12
Zero paged,X		LDA $12,X
Absolute		LDA $4232
Absolute,X		LDA $4232,X
Absolute,Y		LDA $4232,Y
Indirect indexed	LDA ($02,X)
Indexed indirect	LDA ($02),Y
Indirect (for jumps)	(START)

The most of the 65xx-instrucions don't work with all
adressing modes. But Genesis will tell you if the time has come.


2.4.1 Byte/Word Syntax
======================

Genesis accepts following syntax:

Definition		Example:
-----------------------------------
decimal 		LDA #1
hexadecimal		LDA #$a4
binary			AND #%01001001
octal			ORA #!732
character		LDY #"a"
	or		LDA #"""
	or even 	STA "21" ;the first char defines the high byte


If you only want to use the higher or the lower byte of a word
just type following signs before typing a constant or label :
'>' for the higher byte.
'<' for the lower byte.

Examples:		LDA <screen
			STA screenpointer1
			LDA >screen
			STA screenpointer2
			LDY #0
			LDA (screenpointer),Y


2.4.2 arithmethic operands ...
==============================

Genesis accepts following operands to make programmer's live easier :

Defintion	 Example
==========================
add		 label + 123
subtract	 label - 123
multiply	 label * 16
divide		 label / 16
AND		 label & $ff
OR		 label | $%1010000000000000

And now a weird example:

label		lda <screenposition+!0345-willy|1211/2*5&%01110110101|2


2.5 Comments
===============

After a comment flag (";") you're able to write any kind of text. 
And now for example (yes, I'm a lazy one ):

hallo	sta $d018	; writes accumulator to a VIC register


2.6 Directives
===============

Yes, Genesis understands some :

ORG <word>[,<word>]	; Defines the actual code position.
			; The first ORG defines the starting adress
			; of the code, the last instructions after
			; the last ORG defines the ending position.
			; With the second operand you can assemble
			; code for another position <word>.
ORG ,<word>		; <- Leaves the real position.

label EQU <word> or	; Defines a label with a word. You can also use
label =   <word>	; it for immediate adressed instructions if
			; it has got byte size.
			; flag=255
			; LDA #flag

BYT <byte1>,<byte2>,... ; Writes byte(s) to actual position.

WOR <word1>,<word2>,... ; Does the same with words.

ASC "Text"		; Does the same with ASCII texts
ASC "Text",<value>	; You can only use byte values with the ASC-Kommand

LST label		; Prints definition of label to screen at
			; assembly.

SYS label		; Creates a the line "0 SYS <label's def> for a
			; CBM-BASIC program.
			; This command also includes an ORG $801.
			; The following code starts at $80f

EXT "filename.asm"	; Includes A65-files.
			; EXT commands in include-files work, too.

EXB filename.bin	; Includes binary files to your code.

Following directives only exist in the full version :

macroname MAC BYT,WOR,WOR   ; Defines a macro
.EM			    ; 
label MAC macroname	    ; Calls macro

.IF/ELS/END/NOT/OR/AND	    ; Comparisons for macro structure
			    ; at assembly only.


3 Error messages
======================

... explain themselves.
The full version inserts error messages to your source code and erases
them if the errors have been removed.
This shareware version just prints error messages to your screen.

Appendix A
==========

6510-CPU instruction set in alphabetic order
---------------------------------------------

ADC	Add memory to accumulator with carry flag
AND	"AND" memory with accumulator
ASL	Shift left one bit (memory or accumulator)

BCC	Branch on carry clear
BCS	Branch on carry set
BEQ	Branch on result zero
BIT	Test bits in memory with accumulator
BMI	Branch on result minus
BNE	Branch on result not uero
BPL	Branch on result plus
BRK	Force break
BVC	Branch on overflow clear
BVS	Branch on overflow set

CLC	Clear carry flag
CLD	Clear decimal mode
CLI	Clear interrupt disable bit
CLV	Clear overflow flag
CMP	Compare memory and accumulator
CPX	Compare memory and index X
CPY	Compare memory and index Y

DEC	Decrement memory or accu by one
DEX	Decrement index X by one
DEY	Decrement index Y by one

EOR	"exclusive-OR" memory with accumulator

INC	Increment accu or memory by one
INX	Increment index X by one
INY	Increment index Y by one

JMP	Jump to new location
JSR	Jump to new location saving return adress

LDA	Load accu with memory
LDX	Load index X with memory
LDY	Load index Y with memory
LSR	Shift right one bit (memory or accumulator)

NOP	No operation

ORA	"OR" memory with accumulator

PHA	Push accumulator on stack
PHP	Push processor status on stack
PLA	Pull accumulator from stack
PLP	Pull processor status from stack

ROL	Rotate one bit left (memory or accumulator)
ROR	Rotate one bit right (memory or accumulator)
RTI	Return from interrupt
RTS	Return from subroutine

SBC	Subtract memory from accumulator with carry flag
SEC	Set carry flag
SED	Set decimal mode
SEI	Set interrupt disable flag
STA	Store accumulator in memory
STX	Store index X in memory
STY	Store index Y in memory

TAX	Transfer accumulator to index X
TAY	Transfer accumulator to index Y
TSX	Transfer stack pointer to index X
TXA	Transfer Index X to accumulator
TXS	Transfer Index X to stack pointer
TYA	Transfer index Y to accumulator

Appendix B
==========

Instruction adressing modes and related execution times in clock cycles :
----------------------------------------------------------------------------
	
	Ac/Im	= accu/implied
	It	= immediate
	ZP	= zero page
	ZX	= zero page indexed with X register
	ZY	= zero page indexed with Y register
	Ab	= absolute
	AX	= absolute indexed with X register
	AY	= absolute indexed with Y register
	In	= indirect
	IX	= indexed indirect with X register
	IY	= indirect indexed with Y register

		
		Ac
Instruction	Im It ZP ZX ZY Ab AX AY In IX IY 
------------------------------------------------------------------------	       
ADC		.  2  3  4  .  4  4* 4* .  6  5*
AND		.  2  3  4  .  4  4* 4* .  6  5*
ASL		2  .  5  6  .  6  7  .	.  .  .
BCC		.  .  .  .  .  .  .  .	2# .  .
BCS		.  .  .  .  .  .  .  .	2# .  .
BEQ		.  .  .  .  .  .  .  .	2# .  .
BIT		.  .  3  .  .  4  .  .	.  .  .
BMI		.  .  .  .  .  .  .  .	2# .  .
BNE		.  .  .  .  .  .  .  .	2# .  .
BPL		.  .  .  .  .  .  .  .	2# .  .
BRK		.  .  .  .  .  .  .  .	.  .  .
BVC		.  .  .  .  .  .  .  .	2# .  .
BVS		.  .  .  .  .  .  .  .	2# .  .
CLC		2  .  .  .  .  .  .  .	.  .  .
CLD		2  .  .  .  .  .  .  .	.  .  .
CLI		2  .  .  .  .  .  .  .	.  .  .
CLV		2  .  .  .  .  .  .  .	.  .  .
* = Add one cycle if indexing across page boundary.
# = Add one cycle if branch is taken and
    add one additional if branching operation crosses page boundary.

		
		Ac
Instruction	Im It ZP ZX ZY Ab AX AY In IX IY 
------------------------------------------------------------------------	       
CMP		.  2  3  4  .  4  4* 4* .  .  5*
CPX		.  2  3  .  .  4  .  .	.  .  .
CPY		.  2  3  .  .  4  .  .	.  .  .
DEC		.  .  5  6  .  6  7  .	.  .  .
DEX		2  .  .  .  .  .  .  .	.  .  .
DEY		2  .  .  .  .  .  .  .	.  .  .
EOR		.  2  3  4  .  4  4* 4* .  6  5*
INC		.  .  5  6  .  6  7  .	.  .  .
INX		2  .  .  .  .  .  .  .	.  .  .
INY		2  .  .  .  .  .  .  .	.  .  .
JMP		.  .  .  .  .  3  .  .	5  .  .
JSR		.  .  .  .  .  6  .  .	.  .  .
LDA		.  2  3  4  .  4  4* 4* .  6  5*
LDX		.  2  3  .  4  4  .  4* .  .  .
LDY		.  2  3  4  .  4  4* .	.  .  .
LSR		2  .  5  6  .  6  7  .	.  .  .
NOP		2  .  .  .  .  .  .  .	.  .  .
ORA		.  2  3  4  .  4  4* 4* .  6  5*
* = Add one cycle if indexing across page boundary.


		Ac
Instruction	Im It ZP ZX ZY Ab AX AY In IX IY 
------------------------------------------------------------------------	       
PHA		3  .  .  .  .  .  .  .	.  .  .
PHP		3  .  .  .  .  .  .  .	.  .  .
PLA		4  .  .  .  .  .  .  .	.  .  .
PLP		4  .  .  .  .  .  .  .	.  .  .
ROL		2  .  5  6  .  6  7  .	.  .  .
ROR		2  .  5  6  .  6  7  .	.  .  .
RTI		6  .  .  .  .  .  .  .	.  .  .
RTS		6  .  .  .  .  .  .  .	.  .  .
SBC		.  2  3  4  .  4  4* 4* .  6  5*
SEC		2  .  .  .  .  .  .  .	.  .  .
SED		2  .  .  .  .  .  .  .	.  .  .
SEI		2  .  .  .  .  .  .  .	.  .  .
STA		.  .  3  4  .  4  5  5	.  6  6
STX		.  .  3  .  4  4  .  .	.  .  .
STY		.  .  3  4  .  4  .  .	.  .  .
* = Add one cycle if indexing across page boundary.

		
		Ac
Instruction	Im It ZP ZX ZY Ab AX AY In IX IY 
------------------------------------------------------------------------	       
TAX		2  .  .  .  .  .  .  .	.  .  .
TAY		2  .  .  .  .  .  .  .	.  .  .
TSX		2  .  .  .  .  .  .  .	.  .  .
TXA		2  .  .  .  .  .  .  .	.  .  .
TXS		2  .  .  .  .  .  .  .	.  .  .
TYA		2  .  .  .  .  .  .  .	.  .  .


Appendix C
===========

Undocumented 6502 commands in alphabetical order
------------------------------------------------

Note:	Only the full version of Genesis knows undocumented mnemonics.
	They can be very helpful. For example "LAX"

AAX	ANDs X with A and stores it to memory
ARR	ANDs accu with memory and rotates it right
ASR	ANDs accu with memory and shifts it right
ATS	ANDs accu with memory and sets carry flag if it's signed
AX2	ANDs A and X and $21 and store the result to memory
AY2	ANDs A and Y and $21 and store the result to memory

DCP	DEC and CMP with given adressing mode

HLT	Halts system totally

ISB	INC and SBC with given adressing mode

LAX	Load A and X register with memory

MAX	ANDs memory with X register and stores bits 1-7 to accu
	Bit 0 of A will be the result of A0 AND X0 AND M0

RLA	ROL and AND with given adressing mode

SLO	ASL and ORA with given adressing mode
SPM	Store result of (SP and M) to A, X and SP
SRE	LSR and EOR with given adressing mode
SX0	Stores X register to memory if it's zero

RRA	ROR and ADC with given adressing mode

XAM	Store result of (X and A) to memory and X


Appendix D
===========

Undocumented 6510 commands in order of values
----------------------------------------------

Notes:	In the listing below there are some shortcuts used :
	A = Accumulator
	, X = Index register X , Y = Index register Y , SP = Stackpointer
	, M = byte in Memory , -> = is Stored in.
	The flag settings are, unless other specified,
	calculated in the same way as the intructions they consist of.

value	mnemonic Adressing mode  effect
--------------------------------------------
02	HLT	 -		 Total HALT
03	SLO	 (Ind,X)	 ASL,ORA
04	NOP	 Zeropage	 NOP
07	SLO	 Zeropage	 ASL,ORA
0B	ATS	 Immediate	 AND #$xx,ASL A with only setting flags
0C	NOP	 Absolute	 NOP
0F	SLO	 Absolute	 ASL,ORA

12	HLT	 -		 Total HALT
13	SLO	 (Ind),Y	 ASL,ORA
14	NOP	 Zeropage	 NOP
17	SLO	 Zeropage,X	 ASL,ORA
1A	NOP	 Implied	 NOP
1B	SLO	 Absolute,Y	 ASL,ORA
1C	NOP	 Absolute	 NOP
1F	SLO	 Absolute,X	 ASL,ORA

22	HLT	 -		 Total HALT
23	RLA	 (Ind,X)	 ROL,AND
27	RLA	 Zeropage	 ROL,AND
2B	ATS	 Immediate	 AND #$xx,ROL A with only setting flags
2F	RLA	 Absolute	 ROL,AND

32	HLT	 -		 Total HALT
33	RLA	 (Ind),Y	 ROL,AND
34	NOP	 Zeropage	 NOP
37	RLA	 Zeropage,X	 ROL,AND
3A	NOP	 Implied	 NOP
3B	RLA	 Absolute,Y	 ROL,AND
3C	NOP	 Absolute	 NOP
3F	RLA	 Absolute,X	 ROL,AND

42	HLT	 -		 Total HALT
43	SRE	 (Ind,X)	 LSR,EOR
44	NOP	 Zeropage	 NOP
47	SRE	 Zeropage	 LSR,EOR
4B	ASR	 Immediate	 AND #$xx,LSR A
4F	SRE	 Absolute	 LSR,EOR

52	HLT	 -		 Total HALT
53	SRE	 (Ind,Y)	 LSR,EOR
54	NOP	 Zeropage	 NOP
57	SRE	 Zeropage,X	 LSR,EOR
5A	NOP	 Implied	 NOP
5B	SRE	 Absolute,Y	 LSR,EOR
5C	NOP	 Absolute	 NOP
5F	SRE	 Absolute,X	 LSR,EOR

62	HLT	 -		 Total HALT
63	RRA	 (Ind,X)	 ROR,ADC
64	NOP	 Zeropage	 NOP
67	RRA	 Zeropage	 ROR,ADC
6B	ARR	 Immediate	 AND #$xx,ROR A
6F	RRA	 Absolute	 ROR,ADC

72	HLT	 -		 Total HALT
73	RRA	 (Ind),Y	 ROR,ADC
74	NOP	 Zeropage	 NOP
77	RRA	 Zeropage,X	 ROR,ADC
7A	NOP	 Implied	 NOP
7B	RRA	 Absolute,Y	 ROR,ADC
7C	NOP	 Absolute	 NOP
7F	RRA	 Absolute,X	 ROR,ADC

80	NOP	 Zeropage	 NOP
82	NOP	 Zeropage	 NOP
83	SX0	 (Ind,X)	 0->M if X=0 , No flags set
87	AAX	 Zeropage	 A and X -> M , No flags set
8B	MAX	 Immediate	 M and X -> A (bits 7-1)
				 M0 and X0 and A0 -> A0, No flags set
8F	AAX	 Absolute	 A and X -> M , No flags set

92	HLT	 -		 Total HALT
93	AX2	 (Ind),Y	 A and X and $21 -> M , No flags set
97	AAX	 Zeropage,Y	 A and X -> M , No flags set
9B	AX2	 Absolute,Y	 A and X and $21 -> M , A and X -> SP, No flags set
9C	AY2	 Absolute,X	 A and Y and $21 -> M , No flags set
9E	AY2	 Absolute,Y	 A and X and $21 -> M , No flags set
9F	AX2	 Absolute,Y	 A and X and $21 -> M , No flags set

A3	LAX	 (Ind,X)	 LDA,LDX
A7	LAX	 Zeropage	 LDA,LDX
AB	LAX	 Immediate	 LDA,LDX
AF	LAX	 Absolute	 LDA,LDX

B2	HLT	 -		 Total HALT
B3	LAX	 (Ind),Y	 LDA,LDX
B7	LAX	 Zeropage,Y	 LDA,LDX
BB	SPM	 Absolute,Y	 SP and M -> A,X,SP
BF	LAX	 Absolute,Y	 LDA,LDX

C2	NOP	 Zeropage	 NOP
C3	DCP	 (Ind,X)	 DEC,CMP
C7	DCP	 Zeropage	 DEC,CMP
CB	XAM	 Immediate	 (X and A) - M -> X
CF	DCP	 Absolute	 DEC,CMP

D2	HLT	 -		 Total HALT
D3	DCP	 (Ind),Y	 DEC,CMP
D4	NOP	 Zeropage	 NOP
D7	DCP	 Zeropage,X	 DEC,CMP
DA	NOP	 Implied	 NOP
DB	DCP	 Absolute,Y	 DEC,CMP
DC	NOP	 Absolute	 NOP
DF	DCP	 Absolute,X	 DEC,CMP

E2	NOP	 Zeropage	 NOP
E3	ISB	 (Ind,X)	 INC,SBC
E7	ISB	 Zeropage	 INC,SBC
EB	SBC	 Immediate	 SBC #$xx
EF	ISB	 Absolute	 INC,SBC

F2	HLT	 -		 Total HALT
F3	ISB	 (Ind),Y	 INC,SBC
F4	NOP	 Zeropage	 NOP
F7	ISB	 Zeropage,X	 INC,SBC
FA	NOP	 Implied	 NOP
FB	ISB	 Absolute,Y	 INC,SBC
FC	NOP	 Absolute	 NOP
FF	ISB	 Absolute,X	 INC,SBC


Appendix E
===========

History of Genesis 6510
------------------------

v1.0	-	First release with include files

v1.1/1.2-	Some internal errors have been removed.

v2.0	-	Undocumented instructions of the 6510 CPU and the
		EXB directive are now included.
		The ASC and BYT directive have been extended to do the same.
		Genesis also allows you to use source codes bigger than
		64k.

v2.1	-	Bugfixed and faster but quite the same as V2.0

v2.2	-	The ORG directive has been extended. Now you can define
		and index to the adresses. Very useful.